Solder Pallet Technical Specification:

| Pallet ID | DIP-solder pallet-001 |
| --- | --- |
| Pallet Name | The pallet of Synthetic stone carbon fiber board for DIP Lead tin process |
| Main feature | static-free ; heat-resisting material ; No deformation ; Long service life ; Lead tin process |
| Surface treatment | Select: 1. Require ( ); 2. Not Require ( × ) ; Process category: 1. Sandblasting & anodizing process ( ); 2. Without sandblasting & anodizing process ( ); 3. Teflon anodizing process ( ); 4. Hard anodizing process ( ) Anodizing Color: 1. Original color ( ) 2. Black color ( ) 3. Green color ( ) 4. Pale yellow color ( ) |
| Application | 1. Solder paste printer: ( ) ; 2. Chip Mounter: ( ) ; 3. Reflow soldering: ( √ ) ; 4. Positioning: ( ) |
| Material category | 1. Synthetic stone carbon fiber board: ( √ ) ; 2. Aerospace aluminum alloy: ( ) ; 3. Titanium alloy material: ( ) ; 4. FR4 fiberboard material: ( ) 5. High-Temp silicone adhesive: ( ) ; 6. High-Temp Magnet: ( ) ; 7. High-Temp magnetic steel 0.06mm: ( ) |
| Material model | Synthetic stone carbon fiber board | BLUE: 1. CDM68.650: ( ) 2. CHP760: ( ) |
|  |  | BLACK: 1. CDM-ESD68.910: ( √ ) 2. CAS761: ( ) |
|  |  | GRAY: 1. CDM-ESD68.940: ( ) 2. CAG762: ( ) |
|  | Aerospace aluminum alloy | 1. 7075# : ( ) 2. 6061# : ( ) 3. 5052#: ( ) |
| Thickness | 2mm ( ) 3mm ( ) 4mm ( ) 5mm ( ) 6mm ( √ ) 8mm ( ) |
| Shape & Dimension |  | 1. Pallet length L= PCB length (L1) + 60mm; 2. Pallet width W= PCB width (W1) + 60mm; 3. Specify pallet dimension: Length[ ]×Width[ ]mm Remark: If more than one PCB board panelized in a pallet, the above calculation will be will not be applied. |
| Panelized method | Panelized method required in pallet design: 1. Yes:( ); 2. No: ( √ ) |
|  | Panelized method 1: ( ) | Panelized method 2: ( ) | Panelized method 3: ( ) |
|  | The width between PCBs: [ ]mm, Default is 25mm |
|  | The number of PCB: [ ] X [ ]panelized into one pallet |
| PCB angle on pallet | Longer side of PCB corresponding to the pallet track edge ( √ ) | Shorter side of PCB corresponding to the pallet track edge ( ) | PCB rotation angle ( ) Generally it can be 30 to 45 degrees |
| Positioning pin for holding PCB: |  | SUS304 positioning pin, which is made by CNC machine in fine processing, ensure the PCB and positioning pin at 90 degrees |
|  |  | Height of positioning pin L =PCB thickness (mm) – (0.10m～0.20mm ) |
|  |  | Positioning pin diameterфX=PCB positioning hole diameterфx–0.05mm |
| Pallet heat transfer (Thermal via): Function: prevent chip components do not melt the solder paste | TOP/BOT share, avoid chip component ( ) | Create thermal via at the bottom of SMD components ( ) | Create thermal via at the open area of pallet ( ) |
| Wave solder pallet – open space requirement | PCB BOT component protection ( √ ) | Screw hole protection ( √ ) | Plastic connector pin protection ( √ ) |
| Pallet track edge dimension: |  | Pallet track in the lower part of pallet : H=2mm; W=5mm Please let us know if you have special requirements. |
|  |  | Pallet track in the upper part of pallet : H=2mm; W=5mm Please let us know if you have special requirements. |
| PCB cavity dimension |  | PCB cavity dimension = PCB dimension + 0.10mm / edge |
| PCB cavity depth dimension |  | PCB cavity depth dimension = PCB thickness – 0.10mm |
| The Packet hole for takeoff the PCB |  | In general, four packet hole will be provided, one for each direction Please let us know if you have special requirements. |
| The holddown design |  | Mainly used for SMT wave solder pallet; It includes the following accessories: high temperature plastic holddowns, springs, screws, adhesive thread locking agent |
|  |  | Mainly used for wave solder pallet( √ ) It includes the following accessories: high temperature plastic holddowns, springs, screws, adhesive thread locking agent |
|  |  | Mainly used for wave solder pallet to prevent topside component movement throughout wave solder. It includes the following accessories: high temperature plastic holddowns, springs, screws, adhesive thread locking agent |
| Design of wave solder pallet block tin bar |  | Antistatic FR4 fiberglass board material, dimension:10 x 10mm, 1. Black color ( √ ) ; 2. white color ( ) |
|  |  | Synthetic stone materials, dimension: 6 x 6mm, black color |
|  |  | 5052# Aluminum materials, dimension: 10mm (T) x 13mm (W) |
| Pallet printing information |  | 1. WSTIANMAO LOGO ( √ ) 2. production model ( √ ) 3. Date of manufacture ( √ ) 4. Pallet flow arrow sign ( ) 5. Serial No. ( ) 6. CAD drawing No. ( √ ) 7. ROHS marking ( ) 8. ESD marking ( ) Please let us know if you have special requirements. |
| Required documentation | 1. PCB board ( ) 2. PCBA board ( √ ) 3. PCB GERBER/CAD ( √ ) 4. Pallet sample ( √ ) 5. CAD drawings produced by the customer ( ) 6. Special technical requirements ( ) |
| Production capacity | SMT solder pallet: General processing capacity is 50 vehicles / 36 hours DIP solder pallet: General processing capacity is 50 pallets / 48 hours The above is the processing time within the factory and the logistics & freight time is according to the logistics company |
| Special requirements |  |
| Remark | 1. Please insert a tick symbol “√ ” or a cross symbol“ × ”in a bracket ( ) ; 2. Please put a number in a bracket [ ]; |
| Technical parameters of synthetic material | All the technical parameters of this material is provided by synthetic materials manufacturers, WSTIANMAO does not have the right to decide. |